| Surveying | Curriculum Area: Mathematics and Statistics, Level 5-6 | Strand: Geometry and Measurement |
| --- | --- | --- |
| Achievement Objectives: | Apply trigonometric ratios and Pythagoras’ theorem in two dimensions |
| Learning Intention: | Apply laws of trigonometry to find the location of a set point |

A surveyor marks 2 positions on one side of the Avon River, a metre off the bank, measures 78.10 metres between them, then sets up a theodolite at each position and measures the angles at A & B to 0.

Question; What is the width of the of the Avon River at Point 0?

Baseline = 78.10 metres

Baseline is 1 metre off the river bank

Angle A = 32 degrees
Angle B = 40 degrees

[Use the sine rule to find the unknown sides of the triangle]

# Text boxes

B

A

O

Width of River?

a

b

River bank

River bank

Avon River

Show your working here: